## Slide 1: DHCPv4 & NAT
CSE 421 – Computer Netwroks
Department of Computer Science and Engineering School of Data & Science

## Slide 2: Automatic IP Address Assignment
Address Translation
IP Addressing Services

## Slide 3: Objectives
DHCPv4 Concepts
DHCPv4 Operations
NAT Concepts
  Introduction to NAT
  PAT (NAT Overloading)
  Port Forwarding
How devices get IP addresses automatically
How many devices share one IP
address

## Slide 4
Dynamic Host Configuration Protocol (DHCP)

## Slide 5: Assigning IPv4 Addresses : Static
Every device that connects to a network needs an IP address.
How to assign an IP address to a device?
  Static
  Dynamic
  Static :
      manually assigning ; stays fixed
      used for devices must always be reachable
      Used for: Web servers, Routers, printers etc.

## Slide 6: Dynamic IPv4 Addressing
  Dynamic :
    assigns IP addresses automatically to devices.
    Used for : Laptops,phones, moving devices
    Who does this??
DHCP
Dynamic Host Configuration Protocol

## Slide 7
Static Assignments?
Dynamic Assignments?

## Slide 8: Dynamic Host Configuration Protocol (DHCP)
Used in large organizations
More scalable.
Easier to manage many clients
Usually part of a central server (Windows Server, Linux DHCP, etc.)
Which device runs it?
Common in homes, small offices (SOHO)
Cheaper
Simple to configure
Wi-Fi routers we use at home run DHCP automatically
Servers
Routers

## Slide 9: DHCP Operations

## Slide 10: DHCP Operation - Start
Host A
Host B
Host C
Packet
Packet
Packet
Packet
Packet
DHCP Discover (Broadcast packet)
  Finds the DHCP server(s) on the network.
FFFF-FFFF-FFFF | Host A | 255.255.255.255 | 0.0.0.0 | 67 | 68 | DATA
Dest MAC address | Source MAC address | Dest IP address | Source IP address | Dest Port No | Source Port No | DATA
172.16.4.254
Packet

## Slide 11: DHCP Operation
Packet
Packet
DHCP Offer (Unicast)
  Contains an available IP address to lease
Host A | DHCP Server | 172.16.4.1 | 172.16.4.250 | 68 | 67 | DATA
Dest MAC | Source MAC | Dest IP | Source IP | Dest Port | Source Port | DATA
Host A
Host B
Host C
IP address : 172.16.4.1 Subnet Mask: 255.255.255.0 Default Gateway: 172.16.4.254 DNS Server : 172.16.4.160 Lease Time : 3 days

## Slide 12: DHCP Operation
FFFFFFFFFFFF | Host A | 255.255.255.255 | 172.16.4.1 | 67 | 68 | DATA
Dest MAC | Source MAC | Dest IP | Source IP | Dest Port | Source Port | DATA
Packet
Packet
Packet
Packet
Packet
Packet
Packet
Packet
DHCP Request (Broadcast)
  Tells server which address host has accepted
Did not take my IP address, so the address is free….
Took my IP address, so the address is occupied….

## Slide 13: DHCP Operation
Packet
Packet
DHCP Acknowledgement (Unicast)
  Server Gives the OK to host to use the IP address.
Host A | DHCP Server | 172.16.4.1 | 172.16.4.250 | 68 | 67 | DATA
Dest MAC | Source MAC | Dest IP | Source IP | Dest Port | Source Port | DATA

## Slide 14: DHCP Operation (DORA)
IP address : 172.16.4.1 Subnet Mask: 255.255.255.0 Default Gateway: 172.16.4.254 DNS Server : 172.16.4.160 Lease Time : 3 days
Notes: When the client boots (or otherwise wants to join a network), it begins a four-step process to obtain a IP address:

## Slide 15: Steps to Renew a Lease

## Slide 16: DHCP Operation
DHCP works in a client/server mode.
When the client connects, the server assigns or leases an IP address to the device.
The host must contact the DHCP server periodically to extend the lease.
The leasing of addresses assures that addresses that are no longer used are returned to the address pool for use by other devices.

## Slide 17
DHCP RELAY

## Slide 18: DHCP related issues
What is the problem here?

## Slide 19: Problem with DHCP Server not in the same network
PC1 tries to obtain an IP configuration
Broadcast
Routers never forward broadcast packets!
Solution??

## Slide 20
Configure R1 Fa0/0 (the interface that receives the PC1broadcasts) to relay DHCP broadcasts to the DHCP server, use the following commands:
FFFFFFFFFFFF | PC1 | 255.255.255.255 | 0.0.0.0 | 67 | 68 | DATA
R1(config)#interface fa0/0
R1(config-if)#ip helper-address 192.168.11.5
192.168.11.5
R1 Fa0/1 Mac
Known as
DHCP Relay
DHCP Server
Dest MAC | Source MAC | Dest IP | Source IP | Dest Port | Source Port | DATA

## Slide 21
How many devices share one IP
address
Why do we need to share??

## Slide 22: Category of IP Addresses
Two Categories
  Private IP addresses
  Public IP addresses
Private IP Addresses:
Used inside homes, offices, universities
Cannot be used on the internet
Safe and reusable
Assigned manually or via DHCP
Example : Separate three IP ranges
10.0.0.0/8
172.16.0.0/12
192.168.0.0/16

## Slide 23: Category of IP Addresses
Public IP Addresses:
  Used on the internet
  Must be unique globally
  Provided by ISP
  Expensive and limited
  Example : Any IP address not within the above private ranges can be considered a public IP address.

## Slide 24: Public Addresses
Must be unique worldwide
Given by ISPs and regulated by global organizations called Regional Internet Registries (RIRs).
Organizations that owns the public IP can use it on their network.

## Slide 25: WHY??
Why categorise into Public and Private IP addresses?
How does using Private IP addresses help us save IP addresses?
Private addresses cannot be routed in the Internet– Do we want this?
Private Address
Public Address
NAT

## Slide 26: Example: NAT; Sending
DA | SA
209.165.201.1 | 192.168.10.10
R2: I have a packet for the outside network. I must translate the IP address.
DA | SA
209.165.201.1 | 209.165.200.226
209.165.200.226

## Slide 27: Example: NAT; Receiving
DA | SA
209.165.200.226 | 209.165.201.1
R2: I have a packet for the inside network. I must translate the IP address.
DA | SA
192.168.10.10 | 209.165.201.1
209.165.200.226

## Slide 28: Advantages of NAT
  Helps save official IP addresses
  Keeps internal network settings consistent, even when public IP configurations change.
  keeps user and device IPs private from the outside internet, enhancing security.

## Slide 29: Disadvantages of NAT
  NAT increases delays.
  End-to-end IPv4 traceability is lost.
  Can cause problems for some protocols, such as Ipsec, VPN
  Main issue: Does not scale
Notes: NAT Increases Forwarding Delays: NAT adds a small delay because it needs to translate private IP addresses to a public one and vice versa, which takes some extra time.
End-to-End Addressing Is Lost: With NAT, the original source and destination IP addresses are modified, meaning the devices on each end don't see each other's true IP addresses. This affects direct communication.
End-to-End IPv4 Traceability Is Lost: It becomes difficult to trace the path or determine the source and destination of data packets across the internet because NAT modifies the IP addresses in transit.
NAT Complicates Tunneling Protocols: Protocols like IPsec, which secure internet communications, rely on knowing the IP addresses of the endpoints. NAT changes these addresses, which can break or complicate these security protocols.

## Slide 30: PAT (NAT Overload)

## Slide 31: NAT Overload (PAT)
Port Address Translation (PAT) = Real-world NAT
Allows many devices to share one public IP
Uses port numbers to differentiate the devices
Router keeps a table:
Private IP + Port → Public IP + New Port
Each connection becomes unique because of the port
PAT changes both the IP address and the port number.

## Slide 32: PAT Operation
209.165.200.226
SA | DA
209.165.200.226:1555 | 209.165.201.1:80
SA | DA
192.168.10.10:1555 | 209.165.201.1:80
SA | DA
192.168.10.11:1331 | 209.165.202.129:80
SA | DA
209.165.200.226:1331 | 209.165.202.129:80

## Slide 33
209.165.200.226
SA | DA
209.165.201.1:80 | 192.168.10.10:1555
SA | DA
209.165.201.1:80 | 209.165.200.226:1555
SA | DA
209.165.202.129:80 | 192.168.10.11:1331
SA | DA
209.165.202.129:80 | 209.165.200.226:1331
PAT Operation

## Slide 34: PAT Operation
NEXT AVAILABLE PORT NUMBER
192.168.10.11:1444
192.168.10.12:1444

## Slide 35: Packets without Ports
Some protocols (like ICMP) do not have TCP/UDP port numbers
PAT still needs a way to identify each connection
ICMP uses a Query ID to match request reply
PAT uses this Query ID the same way it uses port numbers

## Slide 36: Port Forwarding

## Slide 37: Port Forwarding
Sometimes we need access to services hosted on private IP addresses (like home security cameras or personal web servers) from the internet.
Can we do that?? Why? Why not?

## Slide 38
www.software.com
One Public IP : 200.20.20.4
www.software.com
Configure in Router : If Packet Dest IP 200.20.20.4 :80 => 192.168.10.10
DNS Records for www.software.com => 200.20.20.4
200.20.20.4 : 80
192.168.10.10 : 80
Port Forwarding

## Slide 39: Port Forwarding
Used when a server inside the network has a private IP
Router maps PublicIP:Port to the correct PrivateIP:Port inside the network.
Allows Internet users to access inside services

## Slide 40
Public IP : 112.12.136.14
112.12.136.14 : 27105 ==> 192.168.1.105:27015
Access from outside
Port Forwarding

## Slide 41: The End